# FT-250 Setup

Unlock the keypad (page 9)

- If an icon that looks like a key appears in the lower right corner of the display, press and hold the [F/L] key for one second until the icon disappears.

Set the frequency (page 7)

- Press the [VFO(PRI)]  key if necessary until “A” or”b” appears in the lower left corner of the display to select the VFO mode.

- Enter the desired frequency using the keypad.  Do not enter the leading “1”, or the decimal point.  For example, enter 146.5200 MHz as 46520.

Set the offset (page 8)

- The radio does this automatically if  Automatic Repeater Shift is enabled and the frequency lies in a repeater subband .

- To override the automatic setting, press the [F/L] key then press the [4(RPT)] key.  Rotate the DIAL knob until –RPT (minus offset) or +RPT (plus offset) or SIMP (no offset, or simplex mode) appears in the display.  Press PTT to save the setting.

Note: The offset is the difference between the transmit and receive frequencies and is required only when operating through a repeater.

Set the CTCSS/PL (page 15)

- Press the [F/L] key then the [1(SQ TYP)] key.  Rotate the DIAL knob until a small “T” appears in the upper center of the display or “TN ENC” appears in the middle of the display.  Press the PTT switch to save this setting.

- If a PL tone is required, press the [F/L] key, and then the [2(CODE)] key.  Rotate the DIAL until the desired tone frequency appears in the display.  Press the [F/L] key to save the setting.

Save the settings (page 18)

- Press and hold the [MR/MW(SKIP)] key until a beep is heard (about one second).

- Within 5 seconds of releasing the [MR/MW(SKIP)] key, rotate the DIAL knob until the desired memory channel number (flashing) appears at the left side of the display, then immediately press the [MR/MW(SKIP)] key again and wait for a long beep.  This stores the settings into the desired memory channel.

Change the Control-Lockout Mode (page 9)

Perform this optional setup one-time only so that the keypad and the DIAL knob are both locked when Keyboard Locking is invoked.  Otherwise, only the keypad will be locked and the DIAL knob will not be locked.

- Press the [F/L] key momentarily, then the [0(SET)] key.

- Rotate the DIAL knob until “32 LK MODE” appears in the display.

- Press the [F/L] key momentarily.

- Rotate the DIAL knob until “K + D” appears in the display.

- Press the PTT switch momentarily to exit to normal operation.

Lock the keypad (page 9)

- Press and hold the [F/L] key for one second.  The key icon will appear in the display.

## Notes

1. The [F/L] key enables the alternate function of each key (yellow letters above the keys).  When in effect, the letter “F” will appear in the lower left corner of the display.  After approximately 5 seconds, the “F” will disappear and the keys will return back to their normal function (black letters). The [F/L] key also locks and unlocks the keypad if held down for about one second.

2. If you make a mistake while programming, simply turn the radio off and back on again.

Saratoga Communication

| Memory Channel | Simplex/ Duplex | Frequency | Offset | Tone Encode |
| --- | --- | --- | --- | --- |
|  | Duplex | 146.655 | Minus | 114.8 |
|  | Simplex | 146.655 | None | 114.8 |
|  | Simplex | 146.505 | None | N/A |
|  | Simplex | 146.595 | None | N/A |