FT60R Quick Setup

1.  Unlock the keypad:

If a padlock appears in the lower left corner of the display,

Press [F/W] key momentarily.

Press [6 LOCK] key momentarily.

Padlock disappears from lower left corner of the display.

2.  Select the frequency band:

Press [V/M] key momentarily until the memory channel number disappears from the

display, indicating VFO mode (aka manual tuning mode).

Press  [BAND] key momentarily until desired band (around 144 MHz or 430MHz) is selected.

3.  Set the frequency:

Enter the desired frequency from the keypad.

4.  Select the repeater shift:

Press [F/W] key momentarily.

Press [0 SET] key momentarily.

Rotate the DIAL knob to select item 38: RPT.MOD.

Press [F/W] key momentarily.

Rotate the DIAL knob to select the desired shift:

RPT. – (negative offset), RPT. + (positive offset), RPT.OFF (simplex)

Press the PTT switch momentarily to save the setting.

5.  Configure CTCSS (aka PL Tone):

Press [F/W] key momentarily.

Press [1 SQ/TYP] key momentarily.

Rotate the DIAL knob to select TONE.

Press the PTT switch momentarily to save the setting.

Press [F/W] key momentarily.

Press [2 CODE] key momentarily.

Rotate the DIAL knob until the display indicates the desired CTCSS tone frequency.

Press [F/W] key momentarily to save the setting.

6.  Select the power level (optional):

Press [F/W] key momentarily.

Press [3 TX PO] key .

Display shows the current setting.

Rotate the DIAL knob to select the desired output level:

HIGH (5 W), MID (2 W), LOW (0.5W)

Press the PTT switch momentarily to save the setting.

7.  Disable WIRES:

The WIRES symbol (two interlocking ovals) will appear in the upper right corner of the display.

Momentarily press the [0 SET] key to cycle it on and off.

Leave it off.

8.  Store settings into memory:

Press and hold [F/W] key for about one second until the display flashes.

Either press [F/W] momentarily to save the settings into the next available memory channel,

Or, within 5 seconds, rotate the DIAL knob to select the desired memory channel,

then press [F/W] momentarily to save the settings.

9.  Return to Memory mode:

Press [V/M] key momentarily.

Memory channel appears in display.

10.  Lock the keypad:

Press [F/W] key momentarily.

Press [6 LOCK] key momentarily.

Padlock appears in lower left of display.

This prevents any accidental changes.

Note:  The Saratoga Amateur Radio Association (K6SA) repeaters are on (1) 146.655 MHz, negative offset, PL (CTCSS Tone Frequency) of 114.8 Hz and (2) 443.150 MHz, positive offset, PL of 100.00 Hz.  The repeaters are normally “linked”, therefore any activity on one repeater is replicated on the other.

Prepared by:

Don Steinbach – AE6PM

ae6pm@arrl.net

(408) 867-3912

Revised 2/23/2011